Checklist for towing/using Chilly Dip

Book the boat with the boat officer.

The standard deposit for any trip using the Club’s boat is £20. The deposit for the club boat may be taken out of this.

Make arrangement with the boat officer to collect the boat and ancillary equipment.

Pick up boat & gear from the boat officer, check it off

Ensure that your car is within spec to tow boat, use spreadsheet

Confirm slipway access at low tides

All arrangements must be advised to the Diving Officer

# Picking up the Boat

Remove covers and store at farm. (These may go with the boat if you wish)

Raise the leg of the engine and secure with the transit frame.

Disable electrics with electrical isolator

Ensure the tubes are firm.

Ensure winch strap is locked off, and painter rope is tied round winch. Ensure front ratchet strap is also secured

Rear straps are also tight

Remove wheel clamp and place in car, or secure in boat so that it does not cause damage on trip.

Hitch onto car.

Raise jockey wheel and secure very firmly.

Attach emergency brake cable and electrics, test lights

Fit your own number plate.

Agree the fuel level with boat officer.

Do not fit the hitch lock whilst driving

# Chilly Dip Nose Weight

By travelling with the dry boxes in there brackets, strapping the full emergency fuel can at the back of the bottle rack and stowing the wheel clamp at the back of the boat the nose weight will be reduced to a reasonable level (e.g. 90kg) Anything in the boat must be strapped in.

If additional items are to be placed in the boat for travelling then they must be placed as close a possible to the wheels of the trailer. Remember that you will be making the overall trailer weight heavier and may be exceeding the limits of your car towing capacity.

# Stopping at services/Leaving Boat unattended

Remove dry boxes and lock them in your car, apply wheel clamp

Before going to sea

Remove lighting board, Prop cover, and trailer straps, (Place straps in the Prop cover) untie painter line

Work from the front of the boat to the back.

Check anchor line is secured to the boat and unravelled

Put in electrical isolator cap and turn on electrics

Place keys in ignition and kill cord in place

Check for adequate fuel and the reserve can

Check spare prop is in the console and pump and bailer are on board

Secure rear bung (under board)

Prime fuel line

Pull up elephant’s trunks

Place dry box’s in their racks and secure in with lines (ensure spare ignition keys and kill cord are in one box)

Remove engine travel support

Ensure people are prepped in dry suits to help with launching

Once boat has been launched park trailer and fit wheel clamp.

# At Sea

Leave engine in vertical position for 5 minutes before starting

Ensure tell tale cooling is working as soon as the engine has been started

Ensure everybody has their dive gear

Inform coast guard where you are going, this will also ensure radios are working.

Inform coast guard on your safe return

# When Leaving the boat in the water overnight

Ensure that the boat is on a secure mooring

Ensure there is sufficient line to moor the boat to take into account the rise and fall of tides

If rafting, ensure that mooring lines are also secured to shore as well as moored to inside boat.

(DO NOT TIE LINES TO GRABS RALES ON THE TUBES)

# Recovering

Ensure engine is lifted and dive gear removed

Preferably float or drive the boat onto the trailer, last resort winch it on

# Ensure winch strap is locked off and painter is tied before boat and trailer are pulled forward

# Prepping boat for the road

Put engine support bracket in place

Remove dry box’s (optional)

Lower elephants trunk

Remove rear bung

Turn off and remove electrical isolator switch

Remove front bung

Tie off painter to winch.

Ensure that emergency brake lead is secured

Ensure tubes are firm

Strap the boat down to the trailer

Secure lighting board run cables and test

Fit your own number plate.

Ensure nothing has been left behind

# Returning the boat at the end of the trip

Ensure engine is flushed with use of the muffs. Water coming from tell tale should taste fresh and warm

The boat and trailer are washed down with fresh water

The lighting board removed from its supports

The engine lowered to the upright position

Wheel clamp applied

The handbrake left off

The tubes are fitted with pressure relief valve so leave firm

Agree fuel level with boat officer.

Report any problems or damage to boat officer

# Miscellaneous

| Dimensions on Trailer Height 2.74 Meters 8.98 feet Length 7.10 Meters 23.3 feet Width 2.40 Meters 7.9 feet **Weight 1400 ?kg ** Inc Full fuel tanks, wheel clamp, 12kg of shot, Minimum water in the hull. Exc. dry box’s, spare anchor etc |  |
| --- | --- |